## Slide 1
Jay Peppel, PE
Area Engineer
November 4, 2021
NH 0046(69)288 PCN 05JN
SD Highway 46 in Wagner
March 24, 2020 (Virtual) August 13, 2020 (National Guard Armory)
July 19, 2021 (City Council Chambers)
Public Meeting

## Slide 2
Present Current Proposal
Discuss Comments Received
Gather Additional Comments
Purpose of the Meeting

## Slide 3
Project Limits
Begin Project
End Project
F
Wagner
Front Ave
Main Ave
High Ave
Walnut Ave
SD Hwy 46

## Slide 4
Improve Safety
Poor Pavement Condition
Improve Drainage
Need Pedestrian /ADA Facilities
Why We Are We looking at an improvement project on Hwy 46

## Slide 5
Existing Typical Section

## Slide 6
Modify 4 Lanes to 3 Lanes with Two Way Center Turn Lane
Add Sidewalks
New Storm Sewer
Roadway Lighting
Traffic Signals
Portland Cement Concrete Surfacing
Proposed Improvements

## Slide 7
3 Lane Section
  2-14’ Outside Lane
  1-11’ Two Way Left Turn Lane
  Curb & Gutter
  Concrete Surfacing
Proposed Typical Section

## Slide 8
Traffic analysis – Greatest benefit/cost ratio
Provides safe storage for left turning vehicles
Reduces the number of conflict points for left turning vehicles and vehicles entering the roadway
Reduces the speed differential between vehicles
Boulevard provides separation between vehicles and pedestrians for increased safety
Reduces crossing width for pedestrians
Boulevard provides snow storage during winter so sidewalks can stay clear for pedestrian use
3 Lane Roadway Advantages

## Slide 9
HW 12 – Milbank (2013) – Similar Traffic Volumes
HW 14 – Miller (2013) – Similar Traffic Volumes
HW 12 – Ipswitch (2012) – Similar Traffic Volumes
Comparable Communities to Wagner
4 Lane to 3 Lane Conversion

## Slide 10: HW 12 Milbank

## Slide 11: HW 12 Milbank

## Slide 12
2 Years
Year 1 – Main St to East End of Project
Year 2 – West End of Project to Main St
Open to Traffic
Phased Construction
Business Location Signs
Construction Duration
2.1 Mile Project Length

## Slide 13
FHWA Strategic Objective #1: Save lives by expanding the use of data-driven, systemic safety management approaches and by increasing the adoption of proven safety solutions by all road owners.
  12 Reported Crashes
    4 Intersection Crashes
    3 Rear End Crashes
    2 Side Swipe Crashes
    3 Other types Crashes
  0 Fatalities
  4 involved injuries
5 Year Period
2016 to 2020
  Reported Crash Rate = 1.16
  Statewide Weighted Crash Rate = 1.92 (crashes per million vehicle miles of travel) 2015 through 2019
Urban Principal Arterial
Crash Data

## Slide 14
All crash types: 31% reduction
Fatal/Injury: 37% reduction
Property Damage: 28% reduction
Crash Data – 4 Lane vs 3 Lane

## Slide 15
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Emergency Vehicle Transit
Improved Emergency response time
SDCL 32-26-15 – Yield to emergency vehicle

## Slide 16
Traffic
    2019 ADT = 4,510
    2044 Projected ADT = 6,990
    Truck Traffic = 5.6%

## Slide 17
Traffic Counts
    * Actual traffic data provided in handout

## Slide 18
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Pedestrian Crossings
Reduced pedestrian Crossing Width
Marked crosswalks
  Existing at Walnut, High and Main
  Proposed at Sheridan
Rectangular Rapid Flashing Beacon
Proposed at Walnut and Sheridan

## Slide 19
Extend Pedestrian Facilities
Front Ave
394th Ave
Walnut Ave
High Ave
Main Ave
Wagner
Building &
Supply
Family
Dollar
Valley
Pump &
Casino
Sheridan Ave
Existing: Walnut to Front Ave and Nat Grd Armory
Planned: Wagner Building & Supply and 394th Ave to Valley Pump & Casino

## Slide 20
Pedestrian Facilities
Boulevard Snow Storage
14’ lane provides Separation

## Slide 21
Replace Existing Lighting
  LED
Roadway Lighting

## Slide 22
Traffic Signals
Traffic Signal at SD46 & Main Street will be replaced

## Slide 23
Increased Truck Turning
Accommodates semis with 53’ trailer
High Ave
SD Hwy 46
Front Ave
SD Hwy 46

## Slide 24
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Traffic Speeds
Wider lanes can encourage increased speeds1
Post construction, review and adjust
Existing Radar Feedback Signs
1 FHWA, Road Diet Informational Guide, 1st Edition, 2014

## Slide 25
Estimated Cost: $11.3 million
Tentative Project Schedule
Winter
2021
Final Design
2022 thru
2023
ROW Acquisition
2024 & 2025
Construction
3 Lane Configuration

## Slide 26
Public Input
Please Submit Questions or Comments by
November 18, 2021 to:
Neil Schochenmaier
South Dakota Department of Transportation
700 East Broadway Avenue
Pierre, SD 57501
Neil.Schochenmaier@state.sd.us
Public Meeting Information can be found at:
https://dot.sd.gov/projects-studies/projects/public-meetings

## Slide 27
Comments Received
Two years of construction will kill the businesses in Wagner

## Slide 28
Comments Received
Our crash data is well under the statewide average so why do we have to change?

## Slide 29
Comments Received
Oversized equipment will have trouble due to the decreased pavement width – houses, farm equipment, slow moving vehicles, etc…

## Slide 30
Comments Received

## Slide 31
Comments Received

## Slide 32
Comments Received
Emergency Vehicles will have trouble getting through town with the 3 lane.

## Slide 33
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Emergency Vehicle Transit
Improved Emergency response time
SDCL 32-26-15 – Yield to emergency vehicle

## Slide 34
Comments Received
Garbage Pickup – Currently Hwy 46 is the only way to pick up garbage for houses along Hwy 46.

## Slide 35
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Garbage Collection
SDCL 32-26-7 allows for using center turn lane to pass a stopped garbage truck.

## Slide 36
Comments Received
Traffic Counts – When/Where and how were they taken?

## Slide 37
Comments Received
Traffic backup at the stoplight at Main Street and HW 46 – Will block vehicles getting on HW 46 East and West of stop light.

## Slide 38
Comments Received
School congestion at Hwy 46 & Walnut Avenue - Need to address with stop light or change school traffic flow.

## Slide 39
Comments Received
Pedestrian / Children crossing Hwy 46 at Walnut Avenue along with near the park.

## Slide 40
To provide safe, efficient access to streets and highways
Limit number of direct accesses to major roadways
Pedestrian Crossings
Reduced pedestrian Crossing Width
Marked crosswalks
  Existing at Walnut, High and Main
  Proposed at Sheridan
Rectangular Rapid Flashing Beacon
Proposed at Walnut and Sheridan

## Slide 41
Comments Received
Pedestrian foot traffic during winter months – Pedestrians have to use highway during winter.

## Slide 42
Pedestrian Facilities
Boulevard Snow Storage
14’ lane provides Separation

## Slide 43
Comments Received
Semis turning South on Front & High Avenues

## Slide 44
Increased Truck Turning
Accommodates semis with 53’ trailer
High Ave
SD Hwy 46
Front Ave
SD Hwy 46

## Slide 45
Comments Received
Speed of Semis through town
Traffic needs to slow down coming into town from the West

## Slide 46
Comments Received
Loss of business due to vehicles not being able to get in and out easily
3 Lane will cause more congestion and make roadway more dangerous
Travelers will find another route to get to the Missouri River because of the congestion caused by the 3-lane

## Slide 47
Comments Received
Principal Arterial – Multilane Facility |  |  | 
LOS | Description | Free-Flow Speed (mph) | Density (passenger cars / mile / lane)
A | Free-flow operation | All | ≤ 11
B | Reasonably free- flow operation; minimal restriction on lane changes & maneuvers | All | > 11 - 18
C | Near free-flow operation; noticeable restriction on lane changes & other maneuvers | All | > 18 - 26
D | Speed decline with increasing flows; significant restriction on lane changes & other maneuvers | All | > 26 - 35
E | Facility operates at capacity; very few gaps for lane changes & other maneuvers; frequent disruptions & queues | 60 55 50 45 | > 35 – 40 > 35 – 41 > 35 – 43 > 35 - 45
F | Unstable flow; operational breakdown | 60 55 50 45 | > 45 > 41 > 43 > 45
Hwy 46 Level of Service 2045 – 3 Lane Section – LOS (A)

## Slide 48
Comments Received
Ipswitch - Mayor
Initially people didn’t think traffic would flow as well, but actually I believe it has improved traffic through Ipswitch and made it safer.
I think it makes it easier for emergency vehicles to go thru town.
I have not seen any issues with oversized equipment going thru town.

## Slide 49
Comments Received
Milbank – City Administrator
Traffic flow thru town is very good and don’t get any complaints about Hwy 12 being a 3 lane. Traffic flow is very similar to the existing 4 lane on South end of town
Waste Management picks up garbage on the 3 lane section and have not had any issues with traffic flow and picking up garbage
I have not seen any issues with oversized equipment going thru town. Once again very similar to the flow on the existing 4 lane

## Slide 50
Public Input
Please Submit Questions or Comments by
November 18, 2021 to:
Neil Schochenmaier
South Dakota Department of Transportation
700 East Broadway Avenue
Pierre, SD 57501
Neil.Schochenmaier@state.sd.us
Public Meeting Information can be found at:
https://dot.sd.gov/projects-studies/projects/public-meetings